## Slide 1
DIGITAL LOGIC DESIGN
4-Bit Magnitude
Comparator
Design • Working • Logic equations • Applications
Inputs: A3 A2 A1 A0 and B3 B2 B1 B0
Outputs: A>B, A=B, A<B
2620030638-Akshay
2620030650-Sowrish
2620030652-Rishida
2620030663-Harshitha
GROUP-10

## Slide 2
1. What is a magnitude comparator?
02
A magnitude comparator is a digital electronic circuit that compares two binary numbers and determines which number is greater, which is smaller, or whether they are equal.
For two binary numbers A and B produces three outputs:
A>B: A is greater than B.
A<B: A is less than B.
A=B: A is equal to B.

## Slide 3
Where is it used?
Comparing numbers in computers
Processors and arithmetic circuits
Digital control systems
Checking whether a value is above or below a threshold
A magnitude comparator is a digital logic circuit, not the same as a comparator used to compare magnitudes in other mathematical contexts.
A | B | A > B | A < B | A = B
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1
Truth table for comparatora 1-bit

## Slide 4
2. Design overview
The most significant bit (MSB) is checked first.
03
A₃…A₀
B₃…B₀
4-BIT
COMPARATOR
A > B
A = B
A < B
KEY IDEA
If the first differing bit is in A, the larger bit decides the result.
Bit priority: A₃/B₃ → A₂/B₂ → A₁/B₁ → A₀/B₀
If all four bit pairs match, the numbers are equal.

## Slide 5
3. Logic equations
Use XNOR to detect equal bit pairs, and AND/OR logic to form the outputs.
04
BIT EQUALITY
Eᵢ = Aᵢ XNOR Bᵢ (Eᵢ = 1 when the bits match)
A = B
EQ = E₃ · E₂ · E₁ · E₀
All four corresponding bits must be equal.
A > B
GT = (A₃·¬B₃) + (E₃·A₂·¬B₂)
+ (E₃·E₂·A₁·¬B₁)
+ (E₃·E₂·E₁·A₀·¬B₀)
A < B
LT = (¬A₃·B₃) + (E₃·¬A₂·B₂)
+ (E₃·E₂·¬A₁·B₁)
+ (E₃·E₂·E₁·¬A₀·B₀)
Notation: · = AND, + = OR, ¬ = NOT, XNOR = equality detector

## Slide 6
4. How does it work?
The comparison stops logically at the first unequal bit, starting from the MSB.
05
1
Compare A₃ and B₃
If different, the MSB decides.
2
If equal, compare A₂ and B₂
If different, this bit decides.
3
If still equal, compare A₁ then A₀
Continue toward the least significant bit.
4
If every pair matches
Set A = B to 1; the other outputs are 0.
Only one output is HIGH (1) for any pair of valid inputs.

## Slide 7
5. Example results / truth table
A full 4-bit comparator has 256 input combinations; these examples show each output case.
06
A (binary) | A (dec.) | B (binary) | B (dec.) | A>B | A=B | A<B
1010 | 10 | 0111 | 7 | 1 | 0 | 0
0101 | 5 | 0101 | 5 | 0 | 1 | 0
0011 | 3 | 1000 | 8 | 0 | 0 | 1
1111 | 15 | 0000 | 0 | 1 | 0 | 0
0000 | 0 | 0000 | 0 | 0 | 1 | 0
Remember: 1 = output is true/HIGH; 0 = output is false/LOW.

## Slide 8
6. Applications
Magnitude comparators are used whenever digital hardware must compare values.
07
PROCESSORS
Compare values in ALUs and support decision instructions.
CONTROL SYSTEMS
Check whether a measured value is above or below a limit.
ADDRESS CHECKING
Compare addresses or priority codes in digital circuits.
DIGITAL INSTRUMENTS
Compare counters, timer values, and sensor readings.
SORTING / SELECTION
Choose the larger or smaller number in hardware.
SECURITY / ACCESS
Compare a stored code or numeric ID with an entered value.
A 4-bit comparator is a small building block for larger n-bit comparison circuits.

## Slide 9
Key points to remember
08
• Inputs are two 4-bit unsigned binary numbers: A and B.
• Outputs are A>B, A=B, and A<B.
• Compare from the most significant bit to the least significant bit.
• XNOR gates detect matching bit pairs; AND/OR/NOT logic forms the outputs.
• For any input pair, exactly one output should be HIGH.
Thank you!
7.conclusion